## Slide 1: CST Logic

## Slide 2: normal CST Scenario
torque
time
veh speed
brake
eng speed limit
eng torque front
eng torque rear
normal recu
CST active
standstill
Constant high value or decreasing with veh speed
Active when Softstop calculated standstill
handover to hydraulic brake
For the stage between CST brought the vehicle to standstill and ramping up the hydraulic brake, the electric engines must be able to keep the vehicle in standstill state to handover smoothly which should be realised by engine speed limit = 0

## Slide 3: normal CST Scenario
torque
time
Control Mode
Request Flag
brake
Eng
speed target
eng torque front
eng torque rear
normal recu
CST active
standstill
Control request switched to RPM control when Softstop calculated standstill
handover to hydraulic brake
2= Torque control Mode
1= RPM control Mode
CST request target Speed = 0 to keep vehicle standstill
Control request is torque control

## Slide 4: normal CST Scenario
扭矩
time
电机请求模式
brake
电机目标转速
eng torque front
eng torque rear
舒适制动功能未激活
舒适制动功能激活
车辆静止停车
此时转速请求有效
舒适制动退出后，EHBi/EMB 需要建压保证车辆驻车功能
扭矩控制模式 TarRegTrqCtrlRqst = Request
转速控制模式 TarRpmCtrlRqst = Request
舒适制动转速目标=0 需要电机保证车辆静止。
此时电制动请求有效

## Slide 5: normal CST Scenario
扭矩
time
电机请求模式
机械制动扭矩请求后轴
DrRqdRearShftBrkTorq
VMC 制动扭矩请求
电制动扭矩请求前轴
PrDrvShftDrRqstdTorqDff_FD
电制动扭矩请求后轴
ThScdDrvShftDrRqstdTorqDffHCU_FD
CST功能未激活
CST功能激活
车辆静止停车
此时转速请求有效
方案1：VMC CST功能负责，这个请求目标：
VMCTarBrkTqFrnt=DrRqdFrntShftBrkTorq
VMCTarBrkTqRear= DrRqdRearShftBrkTorq
因为VMC只能通过这两个信号获悉驾驶员制动扭矩目标。所以请求也只能区分前后轴无法单轮请求。
扭矩控制模式 TarRegTrqCtrlRqst = Request
转速控制模式 TarRpmCtrlRqst = Request
此时电制动请求有效
驾驶员请求扭矩与实际车辆减速扭矩一致：
DrRqdFrntShftBrkTorq
DrRqdRearShftBrkTorq
PrDrvShftDrRqstdTorqDff_FD
ThScdDrvShftDrRqstdTorqDffHCU_FD
此时CST实际请求的减速扭矩<驾驶员请求的减速扭矩
机械制动扭矩请求前轴
DrRqdFrntShftBrkTorq
VMCTarBrkTqFrnt=DrRqdFrntShftBrkTorq
VMCTarBrkTqRear= DrRqdRearShftBrkTorq

## Slide 6: normal CST Scenario
扭矩
time
电机请求模式
机械制动扭矩请求
DrRqdFrntShftBrkTorq +
DrRqdRearShftBrkTorq
VMC 制动扭矩请求
电制动扭矩请求前轴
电制动扭矩请求后轴
CST功能未激活
CST功能激活
车辆静止停车
VMC CST功能负责ramp up机械扭矩到驾驶员目标值：
VehTargtDecelBrkTorq=DrRqdFrntShftBrkTorq + DrRqdRearShftBrkTorq
VehTargtDecelBrkTorq 这个信号无需新增，会按照3500Nm/s 的斜率发送这个值给制动。
扭矩控制模式 TarRegTrqCtrlRqst = Request
转速控制模式 TarRpmCtrlRqst = Request
驾驶员请求扭矩与实际车辆减速扭矩一致：
DrRqdFrntShftBrkTorq
DrRqdRearShftBrkTorq
PrDrvShftDrRqstdTorqDff_FD
ThScdDrvShftDrRqstdTorqDffHCU_FD
此时CST实际请求的减速扭矩<驾驶员请求的减速扭矩
起始点：VehTargtDecelBrkTorq=DrRqdFrntShftBrkTorq + DrRqdRearShftBrkTorq
斜率按照3500Nm/s 斜率下降到0.
斜率按照3500Nm/s 斜率从0升到目标。
VehTargtDecelBrkTorq=DrRqdFrntShftBrkTorq + DrRqdRearShftBrkTorq
请求达到目标即可退出CST功能，无需校验实际制动力是否达标。