## Slide 1
Simulation model for SoftStop
PRO24_0006_IBC&EMB-RT for VSS
September 2025

## Slide 2: Simulink Simulation Model
Simplified Vehicle
Dynamic model
Pitch Reference Generator
+
Controller (FB and FF)
Input Data
+
Controller parameters
The Simulink model provides a detailed representation of the modeling and control for SoftStop. It includes both the detailed controller and the simplified model of the vehicle dynamics. The simulation model can be decomposed in 3 main blocks:

## Slide 3: Input Data + Control parameters
The file initializes the model parameters.
It primarily contains the vehicle parameters and the matrices that define the state-space representation of the simplified vehicle model.
The behavior of the controller and the reference generation can be adjusted by modifying the parameters: P, I, D, and N for feedback control, and k1 and k2 for reference generation.
The default values correspond to the nominal values used for the FMU tests in ADAMS.

## Slide 4
Pitch Reference Generator + Controller (FB and FF)
The controller follows the same input/output structure as the tested FMUs. Based on the pitch reference generation and the controller parameters, it takes a deceleration command as input to generate a pitch reference and a force distribution according to the controller parameters.
It supports the same modes of operation:
Feedback: on/off
Rear axle: in-wheel or on-board
Front axle: in-wheel or on-board
On-Board Front | On-Board Rear | Feedback Enabled
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 0
0 | 0 | 1
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1
Feedforward only
Feedforward +
Feedback control
Input Variables | 
Enable control | Activate the control system. When false, the output torques are all 0.
Accel Longitudinal | Desired longitudinal acceleration of the vehicle.
PitchSS k1 | Gain to adjust stationary value of pitch generator
ResponseTime k2 | Gain to adjust time response of pitch generator
Enable On-Board Front | Enables on-board braking on the front axle
Enable On-Board Rear | Enables on-board braking on the rear axle
Feedback Enable | Enables the feedback controller
Theta Measured | Actual pitch angle from vehicle sensors
Proportional | Gain of proportional component of Feedback Ctr
Integral | Gain of integral component of Feedback Ctr
Derivative | Gain of derivative component of Feedback Ctr
FilterCoefficient | Filter coeficient for derivative of Feedback Ctr
Control mode
selector
Sensor measurement
Adjustable
PID
Parameters
Pitch Ref Generator
Parameters
Feed-Forward control law: Parameters … defined in initialization script

## Slide 5
PID Feedback compensator
Brake distribution FF
Pitch trajectory generation (polynomial)
Polynomial calculation
Pitch signal generation
The controller block is composed by the following main blocks:
Pitch trajectory generation:
  Polynomial calculation: Computes a smooth pitch trajectory polynomial based on k1, k2, and the desired deceleration. The polynomial is updated in real time in response to changes in the deceleration command .
  Pitch signal generation: Using the current polynomial, this module generates the corresponding pitch signals, including pitch, pitch rate, and pitch acceleration.
PID Feedback compensator: Computes the feedback component, based on the pitch tracking error.
Brake distribution FF: First, it computes the feedforward braking control based on the pitch and deceleration reference signals. Then, depending on the selected mode of operation (in-wheel or on-board, with or without feedback), it adapts the control by adding feedback if enabled and distributing the braking torque to the outputs accordingly to the mode of operation.
Feed-Forward control law: Parameters … defined in initialization script
Pitch Reference Generator + Controller (FB and FF)

## Slide 6: Simplified Vehicle Dynamic model
Equations for pitch and heave dynamics of sprung mass
+
Pitch Inertia
Pitch stiffness and damping
Heave coupling
Torque from braking forces (in-wheel)
Heave mass
Pitch coupling
Heave stiffness and damping
Torque from braking forces (on board)
Torque from braking forces (in-wheel)
Torque from braking forces (on board)
The simplified model used for the pitch and heave dynamics are the following. This information is coded into a state-space representation in the simulation model.

## Slide 7
¡Thank you!

## Slide 8
主要流程：
信号采集与预处理
  获取驾驶员压力请求、车辆速度、加速度、坡度等信号。
  判断各类信号有效性和系统状态（如Boost状态、信号完整性等）。
软停激活判据
  检查舒适停车开关、Boost系统、信号有效性等，决定是否允许软停。
  检查其他性能子系统（如ABS等）是否激活，防止冲突。
  采用延时机制，避免性能子系统刚退出时立即进入软停。
坡度补偿
  根据坡度查表调整驻车压力，防止车辆在坡道上溜车。
车辆行驶方向判定
  检查所有车轮是否为前进方向，作为软停激活的前提。
状态机管理
  状态包括：OFF、STANDBY、ACTIVE、FAILURE。
  进入ACTIVE状态需满足一系列判据（如压力、速度、加速度、坡度、方向等）。
  状态切换时重置计时器和相关标志。
压力请求计算
  ACTIVE状态下，根据车辆速度、停止状态、加速检测等，动态调整压力请求。
  坡道、滚动、反向驾驶等特殊情况做压力补偿。
  SSM（自动泊车等）特殊场景下，压力请求做斜坡上升。
压力速率限制
  对压力变化速率做滤波和限幅，保证舒适性和安全性。
低Boost检测
  检查Boost压力是否低于阈值，计时后置低Boost标志。
软停结束与复位
  车辆速度高于阈值、压力请求低于阈值、性能子系统激活等，均会退出软停。
  退出时压力做斜坡恢复，防止突变。
轮个体接口
  将压力请求和速率分配到每个车轮，便于后续轮个体控制

## Slide 9
输入读取：从 Db_Input、WhlSpd、ArbBoost/Bhs/PerfMode 等读取车速、车轮转向、坡度、制动踏板请求、Boost 状态、SSM/驻车相关信号等。
激活条件判定：判断是否满足软停触发条件（速度阈、制动踏板释放/接近停止、方向一致性、Boost/系统允许、信号完整性等）。
状态机/计时器：管理 OFF/Standby/Active 等状态，使用定时器防抖与延时退出（避免与其它子系统冲突）。
压力计算：计算每个轮的目标驻车/保持压力（考虑坡度补偿、方向、停止后保持压力、速度相关梯度等）。
速率限制与滤波：对压力上/下调速率进行限幅和平滑，以保证舒适性。
输出与仲裁：将结果写入 DbSoft 结构，并可能与 Arb/Boost/Bhs 等模块协同仲裁。
NVRAM：读取/写回可能的配置或累计计数等。